## Slide 1
SUMMER INTERNSHIP PRESENTATION
Multi-Connectivity and NTN in oCUDU and srsue
Practical Design, Protocol Stack Re-Engineering, and Empirical Validation on Disaggregated 5G Platforms
PRESENTER
Youcef Bellouche
COLLABORATORS
Stefano Taborelli, Pedro B. Velloso, Stefano Secci
INSTITUTIONS
CNAM (Paris)

## Slide 2
Onjective of the internship
First working open-source dual-stack UE implementation.
Validated 6 distinct space-ground deployment architectures.
Modeled full 3GPP Release 17 NTN delays and offsets for LEO and GEO.

## Slide 3
Why oCUDU and srsue?
The Open-Source Imperative
Architectural Match
100% Free architecture. Full access to every layer without proprietary constraints.
Community-driven transparency. Complete inspection of internal protocol states.
Unrestricted refactoring. Deep architectural changes prohibited by commercial stacks.
oCUDU
Disaggregated network side. Clean separation of CU-CP, CU-UP, and DUs across F1 and E1 interfaces.
srsue
Full-stack software UE. Capable of flexible, real-time radio emulation and complex modification.

## Slide 4
Before vs. After
BASELINE STACK
TRANSFORMED STACK
Network Side
Strict 1:1 single connectivity. One CU supervised a single DU.
UE Side
Strictly linear pipeline. One Radio, MAC, RLC, and PDCP layer.
The Deadlock
Dual UE apps caused OS IP address conflicts and collisions.
Network Orchestration
1 CU dynamically orchestrates 2 independent DUs.
Dual Stack
Simultaneous parallel radio legs in one application process.
MR-DC compliant
Shared PDCP memory layer handles splitting and reordering.

## Slide 5
HOW WE MODIFIED THE CODEBASE
Core Engineering Achievements
Unified Execution
Master and secondary connections in one app. Zero Linux namespace conflicts.
In-Memory Delivery
Direct PDCP buffer routing. Zero intermediate network delays or socket overhead.
Control Protection
All vital RLC signaling routed strictly through the isolated master cell.
Standard Compatibility
Operates over standard F1/E1. Zero changes required to the Open5GS core.

## Slide 6
Multi-Connectivity Modalities
Split Bearer
THROUGHPUT AGGREGATION
Packet Duplication
ULTRA-RELIABILITY
Dynamic Switching
INSTANT FAILOVER
Simultaneous distribution across DU1 and DU2.
User-configurable ratios (1:1, 2:7, 3:4).
Active congestion avoidance redirects full queues.
Simultaneous identical transmission across paths.
PDCP accepts first-arrival payload.
Seamless automatic duplicate discard.
100% unilateral routing through active leg.
Secondary leg kept synchronized in background.
Instant ground-to-space failover without teardown.

## Slide 7
NON-TERRESTRIAL NETWORK (NTN) MODELING
3GPP Release 17
3GPP TR 38.821 - Solutions for NR to support non-terrestrial networks (NTN)
Scheduling Offsets
Release 17 slot scheduling offsets prevent uplink grants from expiring prematurely.
Ephemeris Broadcast
SIB19 broadcasts 3D satellite position coordinates and velocities direct to device.
HARQ Optimization
Disabled standard stop-and-wait retransmissions to prevent buffer latency freezes.
Extended Guard Timers
Procedural timers extended from 5 seconds to 12.8 seconds for space propagation.
LEO PROFILE
7 ms
One way delay
600 km altitude • 28,800 software samples.
GEO PROFILE
240 ms
One way delay
35,786 km altitude • 1,382,400 software samples.

## Slide 8
5 Space & Ground Architectures
S. Taborelli, F. Veisi, P. B. Velloso and S. Secci, "O-RAN Integrated Space-Terrestrial Networks: A Multi-Connectivity Strategy Analysis," IEEE INFOCOM 2026, Tokyo, Japan, 2026,

## Slide 9
Empirical Validation Results
Full End-to-End Setup
Integrated Open5GS Core, disaggregated oCUDU nodes, and monolithic dual-stack UE over software radio channels.
Key Architectural Insight
Terrestrial anchoring bypasses strict device delay requirements. Commercial devices instantly attach to the zero-delay ground cell, unlocking high-throughput satellite aggregation immediately.
3–5s Establishment
PDU sessions connect reliably across all scenarios.
Data Verification
End-to-end ICMP ping traffic confirms seamless routing.
50/50 Splitting
Clean packet alternation confirmed in protocol logs.

## Slide 10
Roadmap: Future Research
Dynamic multi-connectivity scerion driven by SINR using collected data.
Integrated constellation dynamic
Physical SDR hardware deployment (USRP).

## Slide 11
CHANNEL PHYSICS & TARGETS
Physical Layer Specifications
0.25 ms Slot Duration (60 kHz)
Numerology 2. A 5ms delay spans 20 slots.
Band n78 Terrestrial (3.5 GHz)
100 MHz bandwidth, TDD architecture.
Band n256 Space (S-Band)
UL: 1980–2010 MHz, DL: 2170–2200 MHz, FDD.
Link Adaptation
SINR dynamically guides base station modulation downscaling (64-QAM to robust QPSK) under poor link conditions.
Disconnection Handling
Loss of satellite visibility triggers internal out-of-sync counters for clean radio link failure and session re-establishment.